## Slide 1: Brain Tumor Detection

## Slide 2: Introduction Methodology Results Table of contents 2 1 3

## Slide 3: Introduction 1

## Slide 4
Brain tumor detection is crucial for early diagnosis and treatment of brain-related diseases. Image processing techniques, including preprocessing, segmentation, feature extraction, and classification, along with machine learning and deep learning algorithms, can enhance early diagnosis and treatment planning. Integrating computer-aided diagnosis systems into clinical workflows can improve efficiency and reliability, leading to improved patient outcomes.

## Slide 5: Methodology
2

## Slide 6
The project focuses on developing an automated system for early detection of brain tumors in MRI images, with an emphasis on timely intervention for improved patient outcomes. The methodology follows a systematic approach:
Image Preprocessing:
  Convert input image to grayscale.
  Apply Gaussian filter for noise reduction and edge enhancement.
  Utilize Otsu's thresholding to create a binary image.
  Implement morphological closing for improved segmentation.
Feature Extraction:
  Capture relevant parameters (area, perimeter, extent, axis lengths, solidity) from labeled image regions.
  Store extracted features in one-dimensional arrays.

## Slide 7
3. Tumor Detection:
  Analyze extracted features to identify the presence of tumors.
Visualization:
  Perform median filtering for noise reduction.
  Apply Canny edge detection.
  Create masks for tumor and non-tumor regions.
  Draw contours on identified tumor regions using a yellow mask.
  Overlay highlighted tumor regions on the original image.

## Slide 8: Results
3

## Slide 9
Final Display:
  Present the original image.
  Display the median filtered image.
  Showcase edge detection results.
  Present the image with highlighted tumors.
Fig(1): If there is a tumor detected
Fig(2): If there is no tumor detected

## Slide 10
.
Fig(3): If there is a tumor detected
Fig(4): If there is no tumor detected

## Slide 11
Thanks
Presented by
Youmna Tarek 202001016
Toka Mohamed 202002280
Reem Amin 202001495
Omnia Lotfy 202000350
Merna Mostafa 202002266